## Slide 1
NON-INVASIVE GLUCOSE · NEAR-INFRARED SPECTROSCOPY
EarSpectro: predicting blood glucose from earlobe NIR spectra
Can multi-wavelength ear spectra predict glucose in people the model has never seen, and which preprocessing, wavelengths, model and calibration make that work?
1050
1200
1450
1550
1650
nm · the five EarSpectro LED wavelengths
github.com/Nishanth-nishu/glycemico-pred · October 2026
Notes: EarSpectro: predicting blood glucose from multi-wavelength earlobe NIR spectra. All results so far come from synthetic data.

## Slide 2
ARCHITECTURE
End-to-end pipeline: raw ear spectrum to glucose, quality and uncertainty
EarSpectro · glycemico-pred · synthetic-data study
2
1
Ear NIR + glucose sync
nearest reading within 5 min
2
Quality control
score Q, reject Q < 0.5
3
Preprocessing
SG · SNV · MSC · d1 · detrend
4
Representation
spectrum, or 45 engineered features
5
Selection
corr · mRMR · RFE · nested λ subsets
6
Models
PLSR · SVR · RF · XGB · CatBoost · FFNN · 1-D CNN
7
Validation
random · unseen-subject · unseen-session
8
Calibration
0–5 reference points per session
9
Explain + output
permutation · SHAP → (Ĝ, Q)
Dark boxes decide whether results generalise: the quality gate, subject-level validation and calibration.
Notes: Each box is a module of the earspectro package. Everything after the split is fitted on training subjects only.

## Slide 3
SIGNAL MODEL AND DATA
Glucose is a tiny part of a mixed spectrum; data is synthetic for now
EarSpectro · glycemico-pred · synthetic-data study
3
Simulates: subject anatomy · sensor placement and gain · OGTT glucose curves · temperature confounder · artifacts · 5% meter error
ear5
5 LEDs, realistic glucose strength
dense
1000–1700 nm every 5 nm, same physiology
control
5 LEDs, 5× stronger glucose, no confounder
Each dataset: 40 subjects × 2 sessions × 16 timepoints × 3 repeats = 3,840 spectra
Glucose band positions: Amerov, Chen & Arnold (2004), Applied Spectroscopy, doi:10.1366/0003702042336136
No real EarSpectro recordings yet; real data plugs into the same CSV format
Notes: Glucose adds about 0.002 OD per 100 mg/dL at its strongest band, against about 0.1 OD of between-subject tissue variation.

## Slide 4
METHODS
Key formulas: quality, preprocessing, features, evaluation and calibration
EarSpectro · glycemico-pred · synthetic-data study
4
Quality score
SNV
MSC
Feature ratio
mRMR selection
1-D convolution
Leak-free split
Accuracy
Fit
Clinical relative error
Offset calibration
Control: ignore spectra
Notes: Every transform, selector and tuning step is fitted inside training folds only.

## Slide 5
RESULTS
Random splits flatter models; 5 LEDs can't untangle glucose
EarSpectro · glycemico-pred · synthetic-data study
5
Chart: R² by split type (dense spectrum)
| PLSR | SVR | CatBoost | FFNN
Random split | 0.42 | 0 | 0.51 | 0.6
Unseen subjects | 0.23 | -0.11 | -0.43 | -0.09
Chart: R² on unseen subjects by dataset
| PLSR | SVR | CatBoost | FFNN
5 LEDs | -0.16 | -0.17 | -0.28 | -0.23
Dense | 0.23 | -0.11 | -0.43 | -0.09
Control (5× signal) | 0.51 | 0.54 | 0.23 | 0.49
FFNN drops from 0.60 to -0.09 on new people. Only linear PLSR stays positive: with 40 subjects, nonlinear models learn the person.
The control proves the pipeline finds real signal (R² ≈ 0.5); 5 LEDs at realistic strength find none.
Notes: Left: dense spectrum, R² by split type. Right: R² on unseen subjects across datasets.

## Slide 6
RESULTS
Calibration, preprocessing, wavelengths, QC and explainability
EarSpectro · glycemico-pred · synthetic-data study
6
Chart: Calibration (dense): MAE vs points
| 0 | 1 | 2 | 3 | 5
PLSR calibrated | 38.3 | 36.1 | 37 | 33 | 25.5
ref_only | 38.3 | 47.3 | 46.5 | 41.4 | 29.7
Chart: Preprocessing (dense): MAE
| Linear | PLSR | FFNN | CatBoost
Raw | 33.7 | 33.8 | 40.9 | 48.2
Best prep. | 32.3 | 32.8 | 31.8 | 32.6
Chart: Wavelengths used (5 LEDs): MAE
| 1 | 2 | 3 | 4 | 5
PLSR (nested) | 44.9 | 44.4 | 46.7 | 45.9 | 46.9
Mean predictor | 43.1 | 43.1 | 43.1 | 43.1 | 43.1
At 5 points optics add ~4 mg/dL (25.5 vs 29.7); with 5 LEDs, none.
Linear barely moves; d1+SNV rescues trees (CatBoost 48 → 33).
No subset of the 5 LEDs beats predicting the mean.
QC
96–100% of artifacts rejected; 0.05% of clean spectra
Explainability
PLSR leans on 1440–1500 nm (water band, temperature), not the 1590 nm glucose band
Clinical
Clarke zone A on unseen subjects: 47% dense PLSR, 57% control SVR
Next
real ear data · more wavelengths · skin-temperature sensor · uncertainty U
Notes: All panels: errors on unseen subjects. ref_only = mean of calibration readings, spectra ignored.